## Slide 1: Energy Efficient Roofing in an Urban Heat Island
Kristen E Brown, PhD
Civil and Environmental Engineering

## Slide 2: Heat

## Slide 3: Urban Heat Island
Klesse College of Engineering and Integrated Design

## Slide 4: Urban Energy Balance

## Slide 5: Urban Energy Balance

## Slide 6: Urban Energy Balance

## Slide 7: Relative Temperature

## Slide 8
Klesse College of Engineering and Integrated Design

## Slide 9: A SEAT at the table—Air Conditioning
  Tolerable
  Affordable
  Environmental
  Supported
Home Renovation
Increased Emissions
Energy Burden

## Slide 12
Kristen.Brown2@UTSA.edu
Notes: Add icons for each department.

## Slide 13
Cool Roofs
Types and Benefits
Presented by: John Follis

## Slide 14: John Follis
18 years Construction & Building Envelope Solutions Issues
  National School Sales & Marketing Manager, Quest Construction
    12 years Fabric Reinforced Acrylic Coating Contractor
      13 years Insurance Defense Attorney
Don’t ask a question when you don’t know the answer.
Anticipate the questions and have the answers.
Tell ‘em what you are going to tell ‘em,
tell ‘em, then tell ‘em what you told them.

## Slide 15: Types of Cool Roofs
TPO
PVC
Fabric Reinforced Coatings

## Slide 18: Same Process Better System

## Slide 19: Installation
Quiet
application process.
No tear offs.
No smells/toxic emissions.

## Slide 20
Varying formula
TPO formulations can vary widely from manufacturer to manufacturer. This is in part due to early trial-and-error attempts to address issues with cracking and other rooftop degradation, and some formulations continue to evolve to this day.
This could be an issue down the road for your TPO roof if, for example, it requires patching or needs to accommodate a new roof penetration. The new TPO membrane may not be completely compatible with the old – even if from the same manufacturer – and may not weld securely.
Not ideal in prolonged heat
Although highly reflective, multiple independent studies in recent years have shown that TPO membranes do not perform well in climates with consistently high temperatures.

## Slide 21
PVC Roofing Pros and Cons
Pro: Strong and Long-Lasting
Engineers create PVC roofs with durability in mind. This strong material’s membrane boasts a long
service life.,
Con: Requires Complete Removal of Old Roof
Contractor might need to entirely remove the old roof.
With this extra work comes extra labor expenses.
Pro: Resistant to Chemicals and Other Hazards
This material can withstand frequent exposure to chemical compounds without wearing down. In
fact, PVC’s strong membrane can also withstand exposure to animal fat from grease vents and
even fire
Con: Problems Occur with Age and Climate
Although PVC roofs can last up to 20 years, you’ll need to account for extra repairs once the roof
reaches 10 years old.
Unfortunately, older PVC is tricky to repair. The hot air welds required for application/repairs don’t
perform as well on older roofs and the new sealants tend to wear away much faster.
You should prohibit foot traffic on your PVC roof when the temperature falls below 50 degrees
Schedule all your maintenance and repairs on a warmer day in the winter, or wait until spring or
summer.

## Slide 22: Fluid Applied
Quiet installation
No Tear offs
Cost effective
Easy to repair
Sustainable

## Slide 23: “
”
Environmental Social
Governance
ESG
IMAGE vs. IMPACT

## Slide 24: The Reports Are In… Corporate America’s Focus
A shift in thinking
Operational Changes - Reassess - Think Differently - Innovate
Sustainability/Reflectivity
Zero Waste Construction
Green House Emissions
Carbon Footprint
Net Zero Energy
Recycling
Water Consumption
Repurpose Buildings
Solar
Renewables

## Slide 25
Waste to the landfill

## Slide 26
Restore vs Tear off
Restore vs Tear Off | Unsustainable to Sustainable | Non Toxic | Zero Waste 397 Dumpsters
$4 vs. $10 | Immediate Savings $2 million vs tear off | Score Rebate | ROI Phase One

## Slide 27
Gravel Roof Renovations 2 years to 1 Grandfathered on Codes
More savings Drains Insulation Noisy but fast

## Slide 28: High Rise Buildings
Staging Costs
Road Closures/Permits Delivery Dumpsters/Removal Loading Costs
Texas Children’s Hospital

## Slide 29: Energy Efficient ROI Phase Two

## Slide 30: Temperature Differential

## Slide 32: Lawrence Berkeley National Lab Test Results
Lawrence Berkeley Study
Location | Description | Insulation | Roof Slope | Roof Covering | Attic | Uncoated Albedo | Coated Albedo | Cooling Energy Savings
Sacramento, California | 1 story residence | R-11 | Flat roof | BUR- Alum. Coating | No | 0.18 | 0.77 | 67%
Sacramento, California | 1 story school | R-19 | Flat roof | Smooth BUR | Yes | 0.08 | 0.68 | 40%
Cocoa Beach Florida | 1 story residence | NONE | Flat roof | Granulated Modified | Yes | 0.20 | 0.73 | 43%
Cocoa Beach Florida | 1 story school | R-19 | Flat roof | Granulated Modified | Yes | 0.23 | 0.67 | 35%
The above table summarizes the results of four studies performed by the Lawrence Berkley National Laboratory in California and Florida. The Albedo of all rooftops were raised by 40 to 60 percentage points well into the range of “very high Albedo” (over 50%). Regardless of the level of insulation in the roof, all buildings showed significant reductions in the amount of cooling energy used (Reductions from 35% to 67%). These studies were all performed on residences or small school buildings.

## Slide 35: Not all white roofs are created equal.
$77 savings per day.

## Slide 36: Tomball Jr. High School Electrical Cost
 | Base year | 1st Year | 2nd Year
Month | 2007-2008 | 2008-2009 | 2009-2010
September | $67,373 | $43,986 | $55,574
October | $56,599 | $51,534 | $48,649
November | $50,987 | $41,870 | $42,934
December | $43,072 | $36,698 | $37,601
January | $48,548 | $41,994 | $37,691
February | $46,440 | $44,042 | $42,319
March | $46,014 | $40,528 | $42,351
April | $53,221 | $47,362 | $39,678
May | $60,395 | $53,807 | $44,520
June | $58,745 | $42,421 | $52,670
July | $28,523 | $47,699 | $42,516
August | $59,622 | $59,973 | $44,146
Total | $619,539 | $551,914 | $530,649
Base Year | 9/07-8/08 | $619,539
1st Year of application | 9/08-8/09 | $551,914
1st Year Savings |  | $67,625 or 20% reduction
Base Year | 9/07-8/08 | $619,539
2nd Y-T-D Totals | 9/09-12/09 | $530,649
2nd Y-T-D Savings |  | $88,890 or 24% reduction
$87,515
Savings since application in Summer of 2008
Electrical cost before and after roofing application.
Note 1: due to change in REP in May 09", electricity rate dropped less than 3%

## Slide 37: Tomball High School Electrical Cost Electrical cost before and after roofing application.
 | Base year | 1st Year | 2nd Year
Month | 2007-2008 | 2008-2009 | 2009-2010
September | $67,373 | $43,986 | $55,574
October | $56,599 | $51,534 | $48,649
November | $50,987 | $41,870 | $42,934
December | $43,072 | $36,698 | $37,601
January | $48,548 | $41,994 | $37,691
February | $46,440 | $44,042 | $42,319
March | $46,014 | $40,528 | $42,351
April | $53,221 | $47,362 | $39,678
May | $60,395 | $53,807 | $44,520
June | $58,745 | $42,421 | $52,670
July | $28,523 | $47,699 | $42,516
August | $59,622 | $59,973 | $44,146
Total | $619,539 | $551,914 | $530,649
Base Year | 9/07-8/08 | $619,539
1st Year of application | 9/08-8/09 | $551,914
1st Year Savings |  | $67,625 or 11% reduction
9/07-8/08
9/09-12/09
Base Year
2nd Y-T-D Totals 2nd Y-T-D Savings
$619,539
$530,649
$88,890
or 14% reduction
$156,515
Savings since application in Summer of 2008
Note 1: due to change in REP in May 09", electricity rate dropped less than 3%
Note 2: Unlike Tomball J.H., this roof was not fully coated; approx. 66% was coated. A 100% coating would have resulted in a much higher cost reduction.

## Slide 38: Tomball – net savings graph

## Slide 39: Low Budget, Low Maintenance
Low-cost repairs performed quickly and easily.
No seams, adhesives, or fasteners.
No heavy equipment.
Repairs can be made by trained maintenance staff.

## Slide 40: Extend Roof Life Span:
Renewable Warranties
Unlike traditional roofing, acrylic-based F.A.S. weather from the top down. A measurable amount of surface millage is lost over the life of the product and can be replaced by additional coatings. Due to the chemistry of a F.A.S., the “regenerated” roof is as strong as the original installation and will last for another set time period depending on the additional coating’s millage.
F.A.S. that utilize a CRRC approved top coating will reduce the surface temperature as well as the internal temperature of a building. Any reduction of roof temperature will prolong the lifespan of not only that F.A.S., but any pre-existing roofs and insulations.
CRRC F.A.S. will also benefit roof mounted HVAC units. Cooler air will be used in the heat exchange, which makes the units more efficient. Reductions in internal temperatures will also decrease usage, prolonging equipment life.
May be eligible for LEED points.

## Slide 41: ROI Phase Three
AguaSeal
Assume cost to renew doubles.
Traditional
Assume cost stays the same.
$7 sq. ft  $10 per sq. ft
Savings: $1.35 Million
Renewal Cost

## Slide 42: ROI for One Life Cycle
$2.1 million No tear off
$2.4 million energy savings
$1.35 million renewal
Total-$7.2 Million

## Slide 43: Weathering

## Slide 44: Wind-FM 4470
Extreme weather resistance
Withstood Super Typhoon Paka
  Sustained winds of 145 mph
  Wind gusts of over 236 mph
All 240+ roofs intact

## Slide 45: Hail-FM-4470

## Slide 46: Heat

## Slide 47: Apps: Details/Accessories
7 Points of Failure
Drains
  Flashing
    Seams
      Penetrations
        Expansion Joints
          Corners
            Perimeter

## Slide 48: Drains

## Slide 49: Wall Details

## Slide 50: Flashing

## Slide 51: Seams

## Slide 52: Seamless
Monolithic

## Slide 53: Penetrations

## Slide 54
Expansion Joints
Expands and contracts with underlying structure.

## Slide 56: Corners

## Slide 57: Perimeter

## Slide 58: Self Adhering

## Slide 59: Warranties
Application Error
Seams, Corners
Failure to Maintain
Assembly System Failure
Drains, Expansion Joints, Penetrations, Flashings
Owner made unauthorized repairs.
Result - Failure Points Not Covered!
AguaSeal NO LEAKS!

## Slide 60
Fluid Applied fabric reinforced roofs are…
Cost Effective
Energy Efficient
Sustainable Roofing
…that eliminates leaks for the life of the building.

## Slide 61: A Roof Like No Other
Your Guide to Rooftop Excellence
© LiveRoof LLC

## Slide 62: Green Roofs Provide Ongoing Cost Benefits and Much More!
© LiveRoof LLC

## Slide 63: Green Roofs Can Turn Ugly Rooftops Into Beautiful Usable Space
© LiveRoof LLC

## Slide 64: Green Roofs Save Money
Extends Roof Life – 2x-3x
Turn a 30 Year Roof Into a 90 Year Roof
.
© LiveRoof LLC

## Slide 65
Stormwater Code Compliance With Benefits
Stormwater compliance means reduced or no water discharge fees.
© LiveRoof LLC

## Slide 66
Reduced Healing Time
Patients with a natural view heal faster and experience less pain.
© LiveRoof LLC

## Slide 67: They Save Energy Green roofs reduce AC costs by approx. 10-75% during hot weather.
© LiveRoof LLC

## Slide 68: Increase Revenue
Visible green roofs can boost rental rates and Increase occupancy.
© LiveRoof LLC

## Slide 69: Boost Solar Output
Evaporative Cooling (from LiveRoof plants) cools the air and makes solar panels 5-15% more efficient.

## Slide 70
Increase Productivity and Prevent Employee “Burnout”
When employees work in more natural environments, stress is reduced and job satisfaction is increased.
© LiveRoof LLC

## Slide 71
Display Stewardship to Foster Goodwill.
Vegetated roofs filter pollutants from runoff before it reaches waterways.
© LiveRoof LLC

## Slide 72: Promote Your Cause Like this cancer treatment hospital.
© LiveRoof LLC

## Slide 73
Expand Usable Space
Rooftop gardens with pathways and patios make buildings more usable.
© LiveRoof LLC

## Slide 74: Retrofit for Posterity
Green Roofs are for Old as well as New buildings.
© LiveRoof LLC

## Slide 75
Green Roofs are Beautiful
© LiveRoof LLC

## Slide 76: LiveRoof Systems
Green Roof Modules
4.25” STANDARD Vegetated Module
6.5” DEEP Vegetated Module
8” MAXX Vegetated Module
RoofBlue
RETAIN
DETAIN
RoofEdge
4.25, 6.5 and 8 inch aluminum edging and corners
RoofStone
Non pedestal paver system

## Slide 77: 4.25” STANDARD Module
Module with soil elevators installed
Engineered soil

## Slide 78: Vegetated Module

## Slide 79
has 2 great options for
Enhanced Stormwater Management
To Reduce Runoff
To Delay Runoff

## Slide 80
RoofBlue RETAIN captures and retains storm water.
Later transfers storm water upward to the plant roots, for plant growth and transpiration (to the atmosphere).
RETAIN™

## Slide 81
University study shows 46% Retention with Standard and 66% when combined with RoofBlue Retain during one year.
Study showed that with medium rain events(.041”-1”) RoofBlue Retain captured over 80% on average.
RETAIN™ REDUCES STORMWATER RUNOFF
RETAIN™

## Slide 82
Maximum Water Holding Capacity of RoofBlue RETAIN module | 2.16 in 1.35 gal/ft2 |  |  | 
LIVEROOF MODULE SIZE | LITE | STANDARD | DEEP | MAXX
Maximum Water Volume Retention (LiveRoof Module + RoofBlue RETAIN) | 3.17 in 2.05 gal/ft2 | 3.91 in 2.45 gal/ft2 | 4.51 in 2.85 gal/ft2 | 5.31 in 3.35 gal/ft2
Design Dead Load (LiveRoof Module + RoofBlue RETAIN) | ≤29.5 lbs/ft2 | ≤41.5 lbs/ft2 | ≤62.5 lbs/ft2 | ≤77.5 lbs/ft2
Total Water Storage of LiveRoof Module and Retain
RETAIN™

## Slide 83
When used with control flow drains, RoofBlue DETAIN expands the usefulness of a green roof system as a stormwater management tool.
Control Flow Drain
RoofEdge
LiveRoof Module
DETAIN™

## Slide 84: Another Effective option from
Delays stormwater
Maximum Water Depth | 3.5 in
Void Space | 90.5%
Maximum Water Volume Detention below the green roof system | 456 in3 / 0.26 ft3 1.97 gal/ft2
Additional design dead load | 18.2 lbs/ft2
DETAIN™
for use with control-flow drains

## Slide 85: RoofEdge® Aluminum Edge Restraint

## Slide 86: RoofStone® Integrated Pavers
Contributes to Stormwater Management: In a recent study, RoofStone pavers retained 25% of annual rainfall.
Integrates with weight, height and dimensions of LiveRoof Standard and Deep modules.
Installs in 1/10th time and labor as traditional pedestal and paver solutions
Eliminates the need for RoofEdge between pavers and modules
Recycled plastic base.

## Slide 87: RoofStone® Integrated Pavers
ADA Compliant when set on pitch of ¼” per 1′ or less.
Size: 24″ L x 12″ W x 4″ H
Weight: 50 lbs
Finish: Beautiful artisan surface, top edge chamfered, sides with chip-preventing, water-conducting standoffs.
LEED Interface: Base of 95% post-industrial polypropylene. Concrete recycled content varies with paver color.
Compressive Strength: 5000+ psi at 28 days; exceeds SPRI standard of 3000 psi by greater than 50%.
Flexural Strength: 770+ psi at 28 days per ASTM C140.
Water Absorption: Less than 5% by cold water method at 28 days per ASTM C140.
Air Content: 4 to 8% maximum.

## Slide 88: RoofStone® Integrated Pavers
RoofStone Paver | Conventional Pedestal & Paver | 
Pedestal | Built-in | Purchased separately
Edging | Not required at green roof interface | Required
Installation | Fast, easy, inexpensive, labor saving | Can be cumbersome and costly

## Slide 89: LoanSTAR Revolving Loan Program
Alamo Area Council of Governments
Revolving loan to finance energy-related, cost-reduction retrofit projects
Cities, counties, independent school districts, state agencies, public institutions of higher education and tax-supported public hospital districts are eligible
Loans repaid from energy cost savings realized by projects. Up to $6 million in financing
Borrower must own and occupy the facility where the proposed retrofit project will occur
Open enrollment begins June 1, 2024
Notes: Should I include what a PEA consists of

## Slide 90: Property Assessed Clean Energy (PACE)
100% long-term, low-cost private financing made possible with assessment lien imposed on property
Commercial, non-profit, industrial & multi-family (5+ units) eligible
Energy efficiency, water conservation, distributed generation, and demand reduction (resiliency) projects eligible
Alamo Area Council of Governments
Chillers, boilers, HVAC, lighting, energy management systems, roofing, windows, doors, insulation, elevator modernization, solar panels, toilets, greywater systems

## Slide 91: EPA Community Change Grants Program
Grant funding for community-driven projects that address climate challenges and reduce pollution while strengthening community engagement
Partnership between community-based non-profit organization and a local government (COG)
Will fund ~150 grants of $10 million - $20 million each
Alamo Area Council of Governments
Notes: Track I will fund approximately 150 large, transformational community-driven investment grants of $10 million - $20 million. Objectives include
• Increasing community resilience through climate action activities
• Reduce local pollution to improve public health
• Center meaningful community engagement
• Build community strength
• Reach priority populations who are acutely exposed to and impacted by climate, pollution, and weather-related threats, and /
or who exhibit acute vulnerabilities to the impacts of environmental pollution.
• Maximize integration across projects
Track II will fund approximately 20 meaningful engagement grants of $1 million - $3 million.
Track II applications should focus on breaking down systemic barriers to community participation in government processes impacting environmental and climate justice.
eligible entity may use a grant awarded under this NOFO for:
1. community-led air and other pollution monitoring, prevention, and remediation, and investments
in low and zero-emission and resilient technologies and related infrastructure and workforce
development that help reduce greenhouse gas emissions1
and other air pollutants;
2. mitigating climate and health risks from urban heat islands, extreme heat, wood heater emissions,
and wildfire events;
3. climate resiliency and adaptation;
4. reducing indoor toxics and indoor air pollution; or
5. facilitating engagement of disadvantaged communities in state and federal advisory groups,
workshops, rulemakings, and other public processes.

## Slide 92: Energy Efficient Commercial Buildings Tax Deduction
Building owners who install energy efficient commercial building property or energy efficient commercial building retrofit property
Must be part of a plan to reduce the buildings total annual energy and power costs by 25% or more
$0.50 per square foot for a building with 25% energy savings
Up to a maximum of $1.00 per square foot for a building with 50% energy savings
CLEAN ENERGY
Notes: Energy efficient commercial building property (EECBP) must be installed on or in a building as part of:
the interior lighting systems,
the heating, cooling, ventilation, and hot water systems, or
the building envelope
Energy efficient commercial building retrofit property (EEBRP) must be installed on or in a qualified building as part of:
the interior lighting systems;
the heating, cooling, ventilation, and hot water systems; or
the building envelope

## Slide 93: Thank You For Your Time!
Alamo Area Council of Governments
Take Our Survey!
Contact Us
Natural Resources Program Administrator
Lyle Hufstetler
lhufstetler@aacog.com
210-376-9901
Natural Resources Outreach Specialist
Mariah Sanchez
msanchez@aacog.com
210-461-8770